## Slide 1
Evaluation of the effects of bandage types on interface pressure and its variation during walking and at rest
1 Thuasne, France
2 Université Jean Monnet, Saint Etienne, France
R. CONVERT1, D. RIMAUD2, A. EL-AOUADI2, P. CALMELS2

## Slide 2
Compression bandages
+
Leg geometry (Chassagne2015)
( = radius of curvature)
Bandage tension (Chassagne2015)
()
Application technique (Rimaud 2014)
(n = number of layers)
Skin-Bandage Coefficient of friction (Chassagne2018) (𝜇)
Interface pressure

## Slide 3
Compression bandages
PLying
PStanding
SSI = PStanding –PSupine
Mechanical properties (Chassagne2016)
(Elastic / Non Elastic)
Superposition(Chassagne2017)
(2 bandages or more)
Application technique(Rimaud2014)
(Spiral, Figure of eight)
SSI
+
Leg geometry variation (Chassagne2018) ( = radius of curvature)
No correlation between SSI and soft tissue mechanical properties variation (Chassagne 2022)
Static Stiffness Index (SSI)
Dynamic Stiffness Index (DSI)
DSI = ΔPWalking
SSI
SSI

## Slide 4
Objectives and Methods (1)
4 compression bandages
  B16 (Thuasne) – Spiral application method with 50% overlap
    Elastic ; ElApplication = 30% ; TApplication = 50 cN.cm-1
  B17 (Thuasne) – Spiral application method with 50% overlap
  Elastic ; ElApplication = 40% ; TApplication = 117 cN.cm-1
  Rosidal K® (RK) (L&R) – Spiral application method with 50% overlap
  Non Elastic ; ElApplication = maximum ; TApplication = 282 cN.cm-1
  Kit Profore ® (KP) (Smith&Nephew) – 4 layer bandages
    Application according to manufacturer recommendations
Objective 1: compare interface pressure during walking with interface pressure in static conditions (supine and standing)
Objective 2 : compare pressure variation during walking with SSI

## Slide 5
Objectives and Methods (2)
15 healthy women
  Age : 21,8 ± 1,9 yo Heigth : 165,7 ± 5,4 cm Weight : 59,1 ± 7,6 kg
Application order of the 4 bandages randomized
Interface pressure in supine et standing positions measured at : t0+5’, t0+25’, t0+45’, t0+65’
Interface pressure during walking measured at : t0+5’, t0+20’, t0+40’, t0+60’
Measurement points : B1 et C with Picopress®
  Static conditions : 3 measurements each time
  Dynamic conditions : measurement for 30s during each sequence ()
Walking speed : 3 km/h
Approved by the ethical commitee of St Etienne

## Slide 6
Interface pressure in static conditions
Chart: Pressure (in mmHg)
| t0+5 | t0+25 | t0+45 | t0+65
B16 | 29.5 | 25.7 | 25.1 | 24.6
B17 | 48.7 | 44.1 | 43 | 42.6
KP | 42.2 | 37.9 | 37.3 | 36.3
RK | 31.8 | 24.3 | 22.8 | 22.1
Chart: Pressure (in mmHg)
| t0+5 | t0+25 | t0+45 | t0+65
B16 | 39.4 | 36.3 | 35.5 | 35
B17 | 58 | 54.2 | 53 | 52
KP | 60.4 | 58.9 | 57.8 | 57.1
RK | 50.5 | 45.9 | 45.3 | 44.1
PStanding > PSupine for all compression bandages
In supine position : PRosidal®K
KP
B16
RK
B17
KP
B16
RK
B17

## Slide 7
Interface pressure in dynamic conditions
Chart: Pressure (in mmHg)
| t0+5 | t0+20 | t0+40 | t0+60
B16 | 32.4 | 30.9 | 30.4 | 29.9
B17 | 51.7 | 49.7 | 48.7 | 48
KP | 51.2 | 49 | 49.2 | 48.4
RK | 35.9 | 33.9 | 32.9 | 31.9
PStanding > PWalking >PSupine for all compression bandages
During walking :
  ≃
KP
B16
RK
B17

## Slide 8
Stiffness Index
8
Chart: SSI (in mmHg)
| t0+5 | t0+25 | t0+45 | t0+65
B16 | 9.9 | 10.6 | 10.3 | 10.4
B17 | 9.2 | 10.1 | 9.9 | 9.4
KP | 18.2 | 21 | 20.5 | 20.8
RK | 18.7 | 21.7 | 22.4 | 22
Chart: DSI (in mmHg)
| t0+5 | t0+20 | t0+40 | t0+60
B16 | 2.2 | 2.4 | 2.3 | 2.3
B17 | 2.7 | 2.8 | 2.7 | 2.6
KP | 4.6 | 4.7 | 4.9 | 5
RK | 4.7 | 4.2 | 4.4 | 4.5
Static Stiffness Index (SSI)
Dynamic Stiffness Index (DSI)
Static Stiffness Index
KP
B16
RK
B17
B16
B17
KP
RK
Dynamic Stiffness Index
  D
  D
DSI = 0,25xSSI

## Slide 9
Discussion (1)
Supine position :
Standing position :
Walking at 3 km/h :
30 healthy volunteers (Stick1989)
Volume of the leg (V)
Variation of the volume of the leg
PStanding > PWalking >Psupine
DSI = 0,25xSSI
SSI >> DSI
Pressure variation during walking is quite low (less than 5 mmHg), and a lot smaller than Static Stiffness Index
18 healthy volunteers (Stick1992)

## Slide 10
Discussion (2)
Effect on veins diameters (Rohan2013, Rohan2014) |  | 
 | Compression | Muscle contraction
Superficial veins | +++ | +
Deep veins | + | +++
Static Stiffness Index and Dynamic Stiffness Index are higher for non elastic compression bandages, and multilayer bandages, than for elastic compression bandages (due to different mechanical behaviours)
The efficacity of compression bandages for venous disorders relies probably on
  The applied pressure
  The capacity of the patient to walk, in order to activate the muscle calf pump
  Pressure variation may have a minor effect

## Slide 11
Bibliography
Chassagne F, Helouin-Desenne C, Molimard J, Convert R, Badel P, Giraux P. Superimposition of elastic and nonelastic compression bandages. J Vasc Surg Venous Lymphat Disord. nov 2017;5(6):851‑8.
Chassagne F, Martin F, Badel P, Convert R, Giraux P, Molimard J. Experimental Investigation of Pressure Applied on the Lower Leg by Elastic Compression Bandage. Ann Biomed Eng. déc 2015;43(12):2967‑77.
Chassagne F, Molimard J, Convert R, Giraux P, Badel P. Numerical Model Reduction for the Prediction of Interface Pressure Applied by Compression Bandages on the Lower Leg. IEEE Trans Biomed Eng. févr 2018;65(2):449‑57.
Chassagne F, Molimard J, Convert R, Helouin-Desenne C, Badel P, Giraux P. Bandages Static Stiffness Index Is Not Influenced by Calf Mechanical Properties but Only by Geometrical Changes. Biomechanics. 2 mars 2022;2(1):87‑94.
Rimaud D, Convert R, Calmels P. In vivo measurement of compression bandage interface pressures: The first study. Ann Phys Rehabil Med. août 2014;57(6‑7):394‑408.
Rohan CPY, Badel P, Lun B, Rastel D, Avril S. Biomechanical response of varicose veins to elastic compression: A numerical study. J Biomech. févr 2013;46(3):599‑603.
Rohan PY, Badel P, Lun B, Rastel D, Avril S. Prediction of the Biomechanical Effects of Compression Therapy on Deep Veins Using Finite Element Modelling. Ann Biomed Eng. févr 2015;43(2):314‑24.
Stick C, Grau H, Witzleb E. On the edema-preventing effect of the calf muscle pump. Eur J Appl Physiol. sept 1989;59(1‑2):39‑47.
Stick C, Jaeger H, Witzleb E. Measurements of volume changes and venous pressure in the human lower leg during walking and running. J Appl Physiol. juin 1992;72(6):2063‑8.